## Slide 1: Long Duration Aeroacoustic Simulation
Dilhara Jayasundara
Advisor: Prof. James Baeder
Department of Aerospace Engineering
AMSC/CMSC-664 – Final Presentation

## Slide 2: Outline
Background
Project Description
    Goals
    ACUM-3
    Non-periodic motion module for CFD
ACUM-3
    Parallelization
        Using GPUs – CUDA
        Using CPUs – MPI
    Computational time optimization
Modifications to CFD
    CFD data output optimization
    Development of non-periodic motion module
Validation
Results
Future Work

## Slide 3: Background
Aeroacoustics
    Why important?
        Emergence of Urban Air Mobility
            Main source of thrust is propellers - - > Propellers are noisy..!
            More air vehicles in urban environments - - > More noise..!
            Passenger and pedestrian discomfort - - > Critical challenge to the industry
        Hybrid-Electric propulsion
            Lower emissions
            Lower fuel usage
            Lower noise..!
        To reduce noise - - > Understand the physics..!
            Flight tests
            Wind tunnel tests
            Computational tools
EcoPulse – Hybrid propulsion aircraft4
NASA X-57 All-electric aircraft5
NASA’s vision on UAM1
Uber Elevate2
Bell Nexus3
Notes: Uber – begin commercial operations in 2023 in LA, Texas and Melbourne

## Slide 4: ACUM
Aeroacoustic Code of the University of Maryland (ACUM)
    Two versions available
        One with compact chord approximation
        One with distributed loads
    Both rely on the periodicity of inputs
    Computes acoustic pressure time history for 1 rotor/propeller revolution
    Cannot handle large amounts of data
    Cannot simulate non-periodic events

## Slide 5: Project Goals
Develop a new version of ACUM that can simulate
    Large amounts of timesteps
    Non-periodic events
        Flyovers
        Take off and landing
        Change in rotor/propeller RPM
        Change in propeller angle of attack
        Simulate urban environments
Modify CFD solver
    Efficient processing of data needed for ACUM
    Simulate non-periodic events
        Non-periodic motion module
Run non-periodic cases

## Slide 6: ACUM-3
Runs on GPUs
    Using CUDA & C++
3-D parallelization
    Observers
    Elements
    Timesteps
      Using binning approach
Operatable on HPC clusters using MPI
    To avoid memory limitations
    Increased processing speed
Ability to process large amounts of non-periodic data

## Slide 7: Algorithm
Read inputs
    Geometric data
    Surface pressure
    Observer locations
Preprocess inputs
    Gaussian and median filters for CFD data
Acoustic pressure computation (parallelized)
    Binning approach
Write output to files
Post process to calculate OASPL at each observer

## Slide 8: Binning Approach for Time Mapping
Observer time loop is not required
Source Time Loop
T
Observer Time Loop
T
T
Interpolation
Binning

## Slide 9: GPU Parallelization
Using CUDA
Used all three dimensions for
    Source elements
    Observers
    Time steps
      Using binning approach
Race conditions
    Multiple GPU threads trying to access the same data at the same time
    Solved by Atomic Addition (Hardware based solution)

## Slide 10: Intermediate Validation
Thickness and Loading noise in dB
For a 4-bladed propeller
Perfect match..!

## Slide 11: Computational Time Optimization
Use of impermeable formulation
    Ffowcs Williams-Hawkings equation has two formulations
        Permeable – imaginary surface around the source
            Requires flow velocity () and local density () at the surface
        Impermeable – actual surface of the source
            Does not require and
            Gaussian and median filters were used to smoothen
    Get rid of data reading and processing by choosing the impermeable formulation
Mesh coarsening
    Surface mesh with tri and quad elements is subdivided to fully quads at mesh generation
    CFD uses this subdivided mesh
    Original mesh is good enough for ACUM (coarsening factor of 3-4)
Use of single precision over double
    Atomic functions require single precision
    Validated for no error
Source

## Slide 12: Computational Time Optimization
4-bladed propeller is considered in the following comparison
    360 time-steps
    181 observers
Upgrade | Computational Time (s) | Reduction in Time | Total Reduction in Time
ACUM-2 | 2462.9 | - | -
ACUM-2 w/ 2D parallelization (excl. time steps) | 531.1 | 78.4% | 78.4%
ACUM-2 w/ Coarsening | 122.6 | 76.9% | 95.0%
ACUM-3 w/ 3D parallelization (binning approach) | 90.0 | 26.6% | 96.3%
ACUM-3 w/ switch to impermeable approach | 57.0 | 89.4% | 97.7%
ACUM-3 w/ switch to single precision | 48.5 | 60.4% | 98.0%

## Slide 13: MPI Parallelization
CFD is set to create one output file per,
    Each surface
    Each chunk of time steps
Each CPU core reads and preprocesses one output file at a time
On a rolling basis (if #cores <= #chunks x #surfaces)
    Different cores read and preprocess different chunks and surfaces
    GPUs can be shared between many CPU cores
        Some cores can read and preprocess inputs while others use GPU
        Same phenomenon as in multi-threading
    Each core writes the computed solutions into 2 large arrays
        For thickness and loading noise
        Accommodates all time steps and observers

## Slide 14: Additional Data Requirement
Binning computation needs each intermediate chunk to have input data for a time step
    After the last time step
    Before the first time
A complete solution is not attained at the two ends of the time history due to non-periodicity
    Truncate the time history based on
        The longest travelling distance at the beginning
        The shortest travelling distance at the end
Longest distance
Observer time
Source
Observer
Incomplete solution
Complete solution

## Slide 15: Validation - Thickness Pressure
4-bladed propeller
For one revolution
At elevation angles
  30 deg
  45 deg
  60 deg
  80 deg
Truncation of time history
0 deg
90 deg
180 deg
270 deg
ACUM-2
ACUM-3

## Slide 16: Thickness Time History Comparison
Three Revolutions
One Revolution

## Slide 17: Flyover Simulation
Propeller is set to fly for 100 revolutions passing a set of observers at
    2R, 5R, 10R, 30R, 60R, 100R, 200R, and 500R from the propeller center normal to the path
        R – Propeller radius
Aerodynamic data needed for only one revolution
    Input files read only at the beginning
    Source location changed for each revolution inside ACUM
Pressure time history was computed for all 100 revolutions
4 CPU cores and GPUs were used in the computation
    Took only 3 minutes
Instantaneous OASPL was calculated using the nearest 360 time-steps
Observers

## Slide 18: Pressure Time History
Total Pressure
Loading Pressure
Thickness Pressure

## Slide 19: Instantaneous OASPL
Observer

## Slide 20: CFD Solvers
“Mercury framework” for in-house CFD
    Supports an overset mesh system that can be solved by different solvers
    GARFIELD solver
        Accelerated using GPU
        Solves structured grids
        Usually used for background and nested meshes (off-body meshes)
    HAMSTR solver
        Solves unstructured grids
        Used for near-body meshes
    TIOGA
        Ensures connectivity between different meshes
        Transfers data between meshes by interpolation

## Slide 21: Mesh Movement
Mercury core performs mesh movements using “Motion” module
    Python/C++ wrapper
    Only performs periodic movements
        Rotation about an axis
        Elastic deflection
    Uses matrix multiplications
    No provisions for
        Acceleration
        Multi-axial rotation
        Translation
    Proprotor transition involves
        Two rotatory motions
          One about the propeller axis
          One about the wing pitch axis
        Accelerated translation
        RPM change to balance the lift

## Slide 22: Motion Matrix Multiplication
Rotation is only available around z-axis
Frame matrix is used to map the rotational axis to z-axis

## Slide 23: New Motion Module
Translation & primary rotation
Secondary Rotation
Primary Rotation
Secondary Rotation

## Slide 24: Accelerated Multi-axial Rotation with One blade
Z - plane
Y - plane
Non-accelerated blades
Accelerated blades

## Slide 25: Translation + Multi-axial Rotation

## Slide 26: Non-Periodic Cases
Transition from hover to cruise
Quasi-steady simulations at
    0 degree
    45 degree
    90 degree
Unsteady simulation from 0 to 90 degrees
    Takes about 5 seconds for transition
    At current RPM of 98.42 Hz, this takes about 85 days to run
    Reducing RPM to 30Hz helps reduce computation time
        Gave negative thrust in cruise due to low RPM
        Insufficient noise levels to investigate
    Used 98.42 Hz with 1 second transition

## Slide 27: Quasi-Steady Case: Hover

## Slide 28: Hover Noise
RPM = 1.3*98.42 Hz
Freestream Mach number (M) = 0

## Slide 29: Comparison with Cruise
Hover rotated by 90 deg. to align with cruise
Both in the actual orientation

## Slide 30: Quasi-Steady Case: 45 deg.

## Slide 31: Vorticity Comparison
Cruise
45 degree
Hover

## Slide 32: Acoustic Results
Hover and 45 deg. rotated to align with cruise
RPM = 1.15*98.42 Hz
M = 0.04

## Slide 33: Quasi-Steady Total Noise

## Slide 34: Coefficient of Thrust Comparison

## Slide 35: Transition
Uses a 2o time step
Rotational speed reducing from 1.3*98.42Hz to 98.42Hz
Transition speed – 0.9o per revolution
Forward speed increasing from M=0 to M=0.08
Constant time step size = dt in 45 deg case
    equivalent to RPM = 1.15*98.42 Hz

## Slide 36: Vorticity Contour
Wake interacts with blade
Creates unsteady loading
Leads to loading noise

## Slide 37: Time History
Azimuth / rad
pT / Pa
Thickness Pressure
Larger oscillations for transition
ACUM is set to run with a constant rotational speed
  Uses azimuth step instead of time step
  Calculated time step size based on omega is higher than actual
  Therefore, derivatives become larger
Omega is no longer constant

## Slide 38: Thickness Pressure Time History
ACUM problem fixed..!
Transition curve amplitude is similar to hover
Radians
Hover

## Slide 39: Thickness Sound Pressure Level
At the observer above the propeller
Reasonably accurate
Transition noise should start below hover
Transition
Hover

## Slide 40: Thank You
Notes: Flops = 181x360x12240x4x(425+360) = 2.5e12