## Slide 1: Long Duration Aeroacoustic Simulation
Dilhara Jayasundara
Advisor: Dr. James Baeder
AMSC/CMSC-663 – Project Proposal

## Slide 2: Outline
Introduction
Binning Approach
Project Goals
Computational Approach
Algorithm
Validation
Deliverables/Timeline

## Slide 3: Introduction
Aeroacoustics
    Why important?
        Emergence of Urban Air Mobility – eVTOLs
            Main source of thrust is propellers - - > Propellers are noisy..!
            More air vehicles in urban environments - - > More noise..!
            Passenger and pedestrian discomfort - - > Critical challenge to the industry
        Hybrid-Electric propulsion
            Lower emissions
            Lower fuel usage
            Lower noise..!
        To reduce noise - - > Understand the physics..!
            Flight tests
            Wind tunnel tests
            Computational tools – computational aeroacoustics
EcoPulse – Hybrid propulsion aircraft4
NASA X-57 All-electric aircraft5
NASA’s vision on UAM1
Uber Elevate2
Bell Nexus3
Notes: Uber – begin commercial operations in 2023 in LA, Texas and Melbourne

## Slide 4: Ffowcs Williams – Hawkings Equation
Rate of change of mass within V,
By divergence theorem,
If f = 0 defines surface S, such that f < 0 in region 1 and f > 0 in region 2,
u – fluid velocity

## Slide 5: Ffowcs Williams – Hawkings Equation
Generalized mass conservation,
Similarly the generalized momentum conservation,
- compressive stress tensor
In region 1,
      Fluid is at rest,
      Density, =
      Pressure
In region 2,
      (Impermeability condition)
gives…..

## Slide 6: Ffowcs Williams – Hawkings Equation
Contribution of Lighthill’s stress tensor can be neglected for subsonic flows
Thickness source – due to displacement of volume by surface
Loading source – due to acceleration of loading
Lighthil’s stress tensor,
Wave equation
Thickness source
(monopole)
Loading source
(dipole)
Quadrupole
source

## Slide 7: Solution to FW-H Equation
Using free-space Green’s function of the wave equation,
      g
Solving
Gives,
– wave operator
Source
Observer
Pressure Wave

## Slide 8: Solution to FW-H Equation
Transform from fixed coordinates y to moving coordinates
Transform from to g
This gives,
Doppler Factor
Notes: 1-Mr is Doppler factor

## Slide 9: Solution to FW-H Equation
Thickness acoustic pressure,

## Slide 10: Farassat’s Formulation 1
Loading acoustic pressure,
Using (proven by differentiating both sides)

## Slide 11: Farassat’s Formulation 1
The observer time derivative needs to be taken numerically
    Increases the execution time on computer
    Reduces accuracy
local angle between surface normal and radiation direction at emission time
As with thickness acoustic pressure we can convert this to retarded time,
Combining formulae for thickness and loading acoustic pressure,
Farassat’s formulation 1
n
r

## Slide 12: Farassat’s Formulation 1A
Taking partial derivative with respect to t,
Therefore the total acoustic pressure can be written as,

## Slide 13: Farassat’s Formulation 1A
After source time differentiation,
    Thickness acoustic pressure
Loading acoustic pressure
- Surface velocity relative to the observer
- Outward unit normal vector of the surface element
- Speed of sound
- Mach number of the source
- Difference between observer () and source ()
- Local force acting on the fluid
- Freestream density

## Slide 14: Computational Aeroacoustics
Sample Source Geometry
Observer locations
Input data
    Geometric data of source surfaces
    Load distribution as surface pressure
    Flow conditions
        Freestream velocity
        Freestream density & pressure
    Observer locations
Output data
    Acoustic pressure at observer locations as a function of time
        Thickness,
        Loading,
Post processing
    Overall Sound Pressure Level (OASPL) in dB

## Slide 15: ACUM8
Aeroacoustic Code of the University of Maryland
Two versions available
    Forward in time approach and double time loop for retarded time calculation
    Both rely on periodicity of input and output
    Can compute acoustic pressure time history for 1 rotor/propeller revolution
    ACUM-1
        Restricted to blade geometries
        Uses Blade Element Momentum Theory for blade load calculations
        Compact chord approximation – spanwise change in loading
    ACUM-2
        No restrictions on geometry
        Uses CFD for load calculations
        Enables use of GPUs for observer and element parallelization
        Time-step parallelization not possible due to double time loop
        Memory limitations

## Slide 16: Forward in Time Approach
for element = 1:Ne
for source time step = 1:Nt
compute acoustic pressure, p
compute observer time, t
end
for observer time step = 1:Nt
map to source time,
compute acoustic pressure, p by interpolation
end
end
Serial
Cannot be parallelized..!
Usually, Nt = 360

## Slide 17: Observer-Source Time Mapping – Double Loop
Observer Time Loop
T
T
Source Time Loop
T
Interpolation

## Slide 18: Long Duration Computations
ACUM uses input data for one propeller revolution
    Makes use of periodicity for
        Derivative computation
        Observer-source time conversion
Cannot simulate non-periodic events
    Propeller RPM change
    Aircraft maneuvers
    Propellers with different RPM
    Flyovers
    Propeller blade/propeller shaft angle of attack change
    Inclusion of urban environment, e.g. Tall buildings
These require computations for at least more than 100 revolutions
    Need time step parallelization

## Slide 19: Binning Approach for Time Mapping
Observer time loop is not required
Source Time Loop
T
Observer Time Loop
T
T
Interpolation
Binning

## Slide 20: Binning Approach – Problem
Double loop approach
    t51 takes 65% from t2 and 35% from t3 = 100% of the solution
Binning approach (single loop)
    t2 provides 70% to t51 and t3 provides 40% to t51
    So altogether, t51 gets 110% of the solution
    t3 provides 60% to t52 and t4 provides 30% to t52
    So altogether, t52 gets 90% of the solution
    This causes an error in the final solution at most time steps
t3
t2
t4
t51
t50
t52
35%
65%
t53
dt
dt
dt
t1
30%
60%
70%
40%
70%
30%

## Slide 21: Modified Binning Approach
ti calculates ti-1 and ti+1 using
    t2 knows t3 – can throw 65% of its pressure into t51
    t3 knows t2 – can throw 35% its pressure into t51
    t51 gets exactly 100% all the time
This makes the time dimension parallelizable
t3
t2
t4
t51
t50
t52
35%
65%
t53
dt
dt
dt
t1

## Slide 22: Project Goals
Develop a new version of ACUM that can process
    Large amounts of timesteps
    Non-periodic data
Modify CFD solver
    Efficient processing of data needed for ACUM
    Simulate non-periodic events
Validation
Run non-periodic cases

## Slide 23: ACUM-3
Runs on GPUs
    Using CUDA or OpenACC
3-D parallelization
    Observers
    Elements
    Timesteps
      Using binning approach
Operatable on HPC clusters using MPI
    To avoid memory limitations
Ability to process large amounts of non-periodic data

## Slide 24: Algorithm
Read inputs
    Geometric data
    Surface pressure
    Observer locations
Preprocess inputs
Acoustic pressure computation (parallelized)
    Binning approach
Write output to files
Post process to calculate OASPL at each observer

## Slide 25: Modifications to CFD
The in-house CFD solver requires capability of
    RPM change
    Non-linear geometric movements
    Angle of attack changes
Dual mesh arrangement
    CFD needs a finer mesh to prevent numerical diffusion and capture small scale turbulent structures
    Acoustic computation can be done on a much coarser mesh
    CFD solver should compute surface pressure on the finer mesh and store on a coarser mesh, which can be accessed by ACUM

## Slide 26: Mesh Generation
The blade surface mesh is generated using Pointwise
    Triangular (unstructured) and quadrilateral (structured) elements – coarser mesh
In-house mesh generation tool is used to generate the volume meshes
    Surface mesh elements are subdivided into pure-quadrilaterals (unstructured) – finer mesh
    Hexahedron volume meshes
Coarser mesh can be used to write pressure and geometric data for acoustic computation

## Slide 27: Blade Mesh (Finer)

## Slide 28: Solution to Periodic Propeller Case
OASPL in dB
Loading Noise
Thickness Noise

## Slide 29: Validation of ACUM - 3
Propeller Model
OASPL/dB
Loading Noise
Thickness Noise
Use a propeller as the source
    Geometry obtained from 1st AIAA Workshop for Integrated Propeller Predictions (WIPP)9
Compute acoustics for one revolution
Compare with the results obtained from ACUM-2
Compute acoustics for multiple revolutions of level-flight
    Periodic output
Compare with ACUM-2 results

## Slide 30: Non-Periodic Cases
Propeller RPM change
    Between 20 Hz – 100 Hz
Propellers with different RPM
    Acoustic pressure amplifications and cancellations with phase difference
Flyovers
    Level flight
    Climb/descent
Aircraft maneuvers
    Turns
    Climbs
    Landing
Propeller shaft/blade angle of attack change
    Helicopter mode to airplane mode and vice versa
First start with propeller blades
Then include
    Spinner
    Nacelle
    Wing
    Fuselage

## Slide 31: Inclusion of Urban Environment
Tall buildings behave like large mirrors for acoustic pressure waves
Model them as reflecting surfaces
    Assign a percentage value for reflectance
Reflecting acoustic pressure will also be added to pressure at observer
Need to assume observer located inside the building
Account for the observer time
Source
Observer
Imaginary Observer
Building
Direct Wave
Reflected Wave

## Slide 32: Timeline
End of November – Finish off coding of ACUM-3
End of December – Complete modifications to CFD
End of January – Propellers with changing RPM
End of February – Change of Propeller/Wing angle of attack
End of March – Aircraft maneuver/flyover simulation
End of April – Inclusion of impermeable building surfaces

## Slide 33: References
https://www.nasa.gov/aero/taking-air-travel-to-the-streets-or-just-above-them/
https://evtol.news/uber-elevate-ecrm-002/
https://www.bellflight.com/products/bell-nexus
https://www.airbus.com/newsroom/press-releases/en/2019/06/daher-airbus-and-safran-team-up-to-develop-ecopulsetm-a-distributed-hybrid-propulsion-aircraft-demonstrator.html
https://www.nasa.gov/specials/X57/index.html
Ffowcs Williams, J. E., and Hawkings, D. L., “Sound Generation by Turbulence and Surfaces in Arbitrary Motion,” Philosophical Transactions of the Royal Society of London. Series A, Mathematical and Physical Sciences, Vol. 264, (1151), 1969, pp. 321–342.
Farassat, F., and Succi, G. P., “The Prediction of Helicopter Rotor Discrete Frequency Noise,” Vertica, Vol. 7, (4), 1983, pp. 309–320.
Amiraux, M., Numerical Simulation and Validation of Helicopter Blade-Vortex Interaction Using Coupled CFD/CSD and Three Levels of Aerodynamic Modeling, Ph.D. thesis, University of Maryland, College Park, 2014.
“Wind Tunnel Testing of Propeller Wingtip Interactions,” Helden Aerospace, LLC and Empirical Systems Aerospace, Inc., 2019.

## Slide 34: Thank You